## Slide 1: CPE 323 Intro to Embedded Computer Systems Assembly Language Programming (Subroutines)
Aleksandar Milenkovic
milenka@uah.edu

## Slide 2: Admin

## Slide 3: The Case for Subroutines: An Example
Problem
  Sum up elements of two integer arrays
  Display results on P2OUT&P1OUT and P4OUT&P3OUT
Example
  arr1 .int 1, 2, 3, 4, 1, 2, 3, 4 ; the first array
  arr2 .int 1, 1, 1, 1, -1, -1, -1 ; the second array
  Results
    P2OUT&P1OUT=0x000A, P4OUT&P3OUT=0x0001
Approach
  Input numbers: arrays
  Main program (no subroutines): initialization, program loops

## Slide 4: Sum Up Two Integer Arrays (ver1)
;-------------------------------------------------------------------------------
; File : Lab5_D1.asm (CPE 325 Lab5 Demo code)
; Function : Finds a sum of two integer arrays
; Description: The program initializes ports,
; sums up elements of two integer arrays and
; display sums on parallel ports
; Input : The input arrays are signed 16-bit integers in arr1 and arr2
; Output : P1OUT&P2OU displays sum of arr1, P3OUT&P4OUT displays sum of arr2
; Author : A. Milenkovic, milenkovic@computer.org
; Date : September 14, 2008
;-------------------------------------------------------------------------------
.cdecls C,LIST,"msp430.h" ; Include device header file
;-------------------------------------------------------------------------------
.def RESET ; Export program entry-point to
; make it known to linker.
;-------------------------------------------------------------------------------
.text ; Assemble into program memory.
.retain ; Override ELF conditional linking
; and retain current section.
.retainrefs ; And retain any sections that have
; references to current section.
;-------------------------------------------------------------------------------
RESET: mov.w #__STACK_END,SP ; Initialize stack pointer
StopWDT: mov.w #WDTPW|WDTHOLD,&WDTCTL ; Stop watchdog timer

## Slide 5: Sum up two integer arrays (ver1)
;-------------------------------------------------------------------------------
; Main code here
;-------------------------------------------------------------------------------
main:

## Slide 6: Sum up two integer arrays (ver1)
;-------------------------------------------------------------------------------
; Stack Pointer definition
;-------------------------------------------------------------------------------
.global __STACK_END
.sect .stack
;-------------------------------------------------------------------------------
; Interrupt Vectors
;-------------------------------------------------------------------------------
.sect ".reset" ; MSP430 RESET Vector
.short RESET
.end

## Slide 7: Subroutines
A particular sub-task is performed many times on different data values
Frequently used subtasks are known as subroutines
Subroutines: How do they work?
  Only one copy of the instructions that constitute the subroutine is placed in memory
  Any program that requires the use of the subroutine simply branches to its starting location in memory
  Upon completion of the task in the subroutine, the execution continues at the next instruction in the calling program

## Slide 8: Subroutines (cont’d)
CALL instruction: perform the branch to subroutines
  SP <= SP – 2 ; allocate a word on the stack for return address
  M[SP] <= PC ; push the return address (current PC) onto the stack
  PC <= TargetAddress ; the starting address of the subroutine is moved into PC
RET instruction: the last instruction in the subroutine
  PC <= M[SP] ; pop the return address from the stack
  SP <= SP + 2 ; release the stack space

## Slide 9: Subroutine Nesting
Main:
MAIN_INS1
MAIN_INS2
MAIN_INS3
CALL SubA
MAIN_INS5
. . .
SubA:
SubA_INS1
SubA_INS2
. . .
CALL SubB
SubA_INSx
. . .
RET
SubB:
SubB_INS1
SubB_INS2
. . .
CALL SubC
SubB_INSy
. . .
RET
SubC:
SubC_INS1
SubC_INS2
. . .
SubC_INSn
. . .
RET

## Slide 10: Mechanisms for Passing Parameters
Through registers
Through stack
  By value
    Actual parameter is transferred
    If the parameter is modified by the subroutine, the “new value” does not affect the “old value”
  By reference
    The address of the parameter is passed
    There is only one copy of parameter
    If parameter is modified, it is modified globally

## Slide 11: Subroutine: SUMA_RP
Subroutine for summing up elements of an integer array
Passing parameters through registers
  R12 - starting address of the array
  R13 - array length
  R14 – returns sum

## Slide 12: Subroutine: SUMA_RP
;-------------------------------------------------------------------------------
; File : Lab5_D2_RP.asm (CPE 325 Lab5 Demo code)
; Function : Finds a sum of an input integer array
; Description: suma_rp is a subroutine that sums elements of an integer array
; Input : The input parameters are:
; R12 -- array starting address
; R13 -- the number of elements (>= 1)
; R14 –- returns sum
; Output : No output
; Author : A. Milenkovic, milenkovic@computer.org
; Date : September 14, 2008
;------------------------------------------------------------------------------
.cdecls C,LIST,"msp430.h" ; Include device header file
.def suma_rp
.text

## Slide 13: Subroutine: SUMA_RP
suma_rp:
clr.w R14 ; clear register R14 (keeps the sum)
lnext: add.w @R12+, R14 ; add a new element
dec.w R13 ; decrement step counter
jnz lnext ; jump if not finished
ret ; return from subroutine
.end

## Slide 14: Main (ver2): Call suma_rp
;-------------------------------------------------------------------------------
; Main code here
;-------------------------------------------------------------------------------
main

## Slide 15: Subroutine: SUMA_SP
Subroutine for summing up elements of an integer array
Passing parameters through the stack
  The calling program prepares input parameters on the stack

## Slide 16: Main (ver3): Call suma_sp (Pass Through Stack)
;-------------------------------------------------------------------------------
; Main code here
;-------------------------------------------------------------------------------
main: bis.b #0xFF,&P1DIR ; configure P1.x as output
bis.b #0xFF,&P2DIR ; configure P2.x as output
bis.b #0xFF,&P3DIR ; configure P3.x as output
bis.b #0xFF,&P4DIR ; configure P4.x as output
jmp $
arr1: .int 1, 2, 3, 4, 1, 2, 3, 4 ; the first array
arr2: .int 1, 1, 1, 1, -1, -1, -1 ; the second array
Address | Stack

## Slide 17: Subroutine: SUMA_SP
;-------------------------------------------------------------------------------
; File : Lab5_D3_SP.asm (CPE 325 Lab5 Demo code)
; Function : Finds a sum of an input integer array
; Description: suma_sp is a subroutine that sums elements of an integer array
; Input : The input parameters are on the stack pushed as follows:
; starting addrress of the array
; array length
; Output : The sum (returned through the stack)
; Author : A. Milenkovic, milenkovic@computer.org
; Date : September 14, 2008
;------------------------------------------------------------------------------
.cdecls C,LIST,"msp430.h" ; Include device header file
.def suma_sp
.text

## Slide 18: Subroutine: SUMA_SP (cont’d)
suma_sp:
; save the registers on the stack
push R7 ; save R7, temporal sum
push R6 ; save R6, array length
push R4 ; save R5, pointer to array
clr.w R7 ; clear R7
lend: pop R4 ; restore R4
pop R6 ; restore R6
pop R7 ; restore R7
ret ; return
.end
Address | Stack

## Slide 19: The Stack and Local Variables
Subroutines often need local workspace
We can use a fixed block of memory space – static allocation – but:
  The code will not be relocatable
  The code will not be reentrant
  The code will not be able to be called recursively
Better solution: dynamic allocation
  Allocate all local variables on the stack
  STACK FRAME = a block of memory allocated by a subroutine to be used for local variables
  FRAME POINTER = an address register used to point to the stack frame

## Slide 20: Subroutine: SUMA_SPSF
;-------------------------------------------------------------------------------
; File : Lab5_D4_SPSF.asm (CPE 325 Lab5 Demo code)
; Function : Finds a sum of an input integer array
; Description: suma_spsf is a subroutine that sums elements of an integer array.
; The subroutine allocates local variables on the stack:
; counter (SFP-2)
; sum (SFP-4)
; Input : The input parameters are on the stack pushed as follows:
; starting address of the array
; array length
; Output : Returns sum (through the stack)
; Author : A. Milenkovic, milenkovic@computer.org
; Date : September 14, 2008
;------------------------------------------------------------------------------
.cdecls C,LIST,"msp430.h" ; Include device header file
.def suma_spsf
.text

## Slide 21: Subroutine: SUMA_SPSF (cont’d)
suma_spsf:
; save the registers on the stack
push R12 ; save R12 - R12 is stack frame pointer
mov.w SP, R12 ; R12 points on the bottom of the stack frame
sub.w #4, SP ; allocate 4 bytes for local variables
push R4 ; pointer register
clr.w -4(R12) ; clear sum, sum=0
lend: pop R4 ; restore R4
add.w #4, SP ; collapse the stack frame
pop R12 ; restore stack frame pointer
ret ; return
.end
Address | Stack

## Slide 22: Performance
Performance(x) = 1 / ExecutionTime(x)
ExecutionTime(x) or ET

## Slide 23: Example: strcopy
Assume:
  R4 contains the address of the source string
  R5 contains the address of the destination string

## Slide 24: MIPS
MIPS - Million of Instructions Per Second
FLOPS – Floating-point Instructions Per Second