## Slide 1: CPE 323 Intro to Embedded Computer Systems Digital-to-Analog Conversion
Aleksandar Milenkovic
milenka@uah.edu

## Slide 2: Admin

## Slide 3: MSP430FG4618 Block Diagram

## Slide 4: DAC – System View
DAC
N
Vout
Analog Output
DAC_DATA
Vref
Binary input

## Slide 5: How does it work?
Multiple implementations
One of the simplest: WEIGTHED RESISTOR DAC
4-bit DAC; Digital input: b3 b2 b1 b0 (b3 is the MSB)
Reference voltage: VR

## Slide 6: 4-bit Weighted Resistor DAC

## Slide 7: R-2R Ladder DAC

## Slide 8: MSP430 DAC12
Modes
  N = 8 (8-bit mode) or N = 12 (12-bit mode) => DAC12RES control bit
  unsigned or straight binary mode (0 – 4095) or signed mode (-2048 – 2047) => DAC12DF
  Voltage output equations for straight binary
  Amplification (1x or 3x) => DAC12IR

## Slide 9: MSP430 DAC12
2 channels (0_OUT, 1_OUT)
Outputs (4618)
  DAC12OPS=0 (0_OUT => P6.6 and 1_OUT => P6.7)
  DAC12OPS=1 (0_OUT => VeREF+, 1_OUT => P5_1)
Reference Voltage
  Internal 1.5 V or 2.5 (from Voltage Gen in ADC12) or external VeREF+

## Slide 10: MSP430 DAC12
Voltage Output
  DAC12_xDAT is double buffered
  When to update output voltage is controlled by DAC12LSEL (latch selection)
    0 – transparent (as soon as you write to into data register it becomes visible to the core)
    1 – DAC data is latched and presented to the core on the next write
    2, 3 – data is latched on the rising edge of the signal coming from from TimerA CCR1 or TimerB CCR2

## Slide 11: MSP430 DAC12
DAC12AMPx control bits configure DAC12 amplifier as follows
  these setting control setting time vs. current consumption of the DAC12 input and output amplifiers

## Slide 12: MSP430 DAC12 Registers

## Slide 13: MSP430 DAC12 Registers

## Slide 14: Example #1
Problem statement: Using DAC12_0 and 2.5V ADC12REF reference with a gain of 1, output 1V on P6.6.
// MSP430xG461x
// -----------------
// /|\| XIN|-
// | | | 32kHz
// --|RST XOUT|-
// | |
// | DAC0/P6.6|--> 1V
// | |
Design:
Step 1: Clocks: ACLK = 32kHz, MCLK = SMCLK = default DCO 1048576Hz, ADC12CLK = ADC12OSC
Step 2: Stop watchdog timer.
Step 3: Ports initialization: P6.6 as special function port (analog output channel A0).
Step 4: DAC12 initialization:
Internal reference voltage (2.5V); software delay to settle down.
Select medium speed/current; DAC12AMPx=5 (101).
Gain should be 1 (DAC12IR=1); Default is gain 3 (DAC12IR=0).
Latch: DAC latches the data when written to DAC12_0DAT (DAC12LSELx=00; default).
DAC12ENC=1 (Enable converter).
Step 5: Software organization. Use TimerA to allow for the internal reference voltage.

## Slide 15: Example #1
#include "msp430xG46x.h"
void main(void)
{
WDTCTL = WDTPW + WDTHOLD; // Stop WDT
ADC12CTL0 = REF2_5V + REFON; // Internal 2.5V ref on
TACCR0 = 13600; // Delay to allow Ref to settle
TACCTL0 |= CCIE; // Compare-mode interrupt.
TACTL = TACLR + MC_1 + TASSEL_2; // up mode, SMCLK
__bis_SR_register(LPM0_bits + GIE); // Enter LPM0, enable interrupts
TACCTL0 &= ~CCIE; // Disable timer interrupt
__disable_interrupt(); // Disable Interrupts
DAC12_0CTL = DAC12IR + DAC12AMP_5 + DAC12ENC; // Int ref gain 1
DAC12_0DAT = 0x0666; // 1.0V
__bis_SR_register(LPM0_bits + GIE); // Enter LPM0
}
#pragma vector = TIMERA0_VECTOR
__interrupt void TA0_ISR(void)
{
TACTL = 0; // Clear Timer_A control registers
__bic_SR_register_on_exit(LPM0_bits); // Exit LPMx, interrupts enabled
}

## Slide 16: Example #2 (Voltage Ramp)
Problem statement: Using DAC12_0 and 2.5V ADC12REF reference with a gain of 1, output positive ramp on P6.6. Use WDT to provide ~0.5ms interrupt used to wake up the CPU and update the DAC with new sample. Use the internal 2.5V Vref.
// MSP430xG461x
// -----------------
// /|\| XIN|-
// | | | 32kHz
// --|RST XOUT|-
// | |
// | DAC0/P6.6|--> RAMP
// | |

## Slide 17: Example #2 (Voltage Ramp)
#include "msp430xG46x.h"
void main(void) {
WDTCTL = WDT_MDLY_0_5; // WDT ~0.5ms interval timer
IE1 |= WDTIE; // Enable WDT interrupt
ADC12CTL0 = REF2_5V + REFON; // Internal 2.5V ref on
TACCR0 = 13600; // Delay to allow Ref to settle
TACCTL0 |= CCIE; // Compare-mode interrupt.
TACTL = TACLR + MC_1 + TASSEL_2; // up mode, SMCLK
__bis_SR_register(LPM0_bits + GIE); // Enter LPM0, enable interrupts
TACCTL0 &= ~CCIE; // Disable timer interrupt
__disable_interrupt(); // Disable Interrupts
DAC12_0CTL = DAC12IR + DAC12AMP_5 + DAC12ENC; // Int ref gain 1
while (1)
{
__bis_SR_register(LPM0_bits + GIE); // Enter LPM0, interrupts enabled
DAC12_0DAT++; // Positive ramp
DAC12_0DAT &= 0x0FFF;
}
}

## Slide 18: Example #2 (cont’d)
#pragma vector = TIMERA0_VECTOR
__interrupt void TA0_ISR(void)
{
TACTL = 0; // Clear Timer_A control registers
__bic_SR_register_on_exit(LPM0_bits); // Exit LPMx, interrupts enabled
}
#pragma vector = WDT_VECTOR
__interrupt void WDT_ISR(void)
{
__bic_SR_register_on_exit(LPM0_bits); // TOS = clear LPM0
}