## Slide 1: CPE 323 Intro to Embedded Computer Systems MSP430 Instruction Set Architecture
Aleksandar Milenkovic
milenka@uah.edu

## Slide 2: Admin

## Slide 3: MSP430 Instruction Set Architecture
1. Types of ISA (16, 16-bit GPRs, R0=PC, R1=SP, R2=SR, R3=CG)
2. Memory View (byte addressable, 16-bit word aligned, little-endian)
3. Data Types (8-bit, 16-bit numbers)
4. Instruction Set
5. Addressing Modes
6. Instruction Encoding
7. Exceptions

## Slide 4: Types of ISA
Stack
Accumulator
Register/memory

## Slide 5: MSP430 Registers
R0
R1
R2
R3

## Slide 6: Address Space
Address space 2^16 bytes
Byte addressable, can read 16-bit words from memory
Words are aligned in memory: start at even addresses
Little-endian placement policy
Flash (ROM): Contains code and constants (read-only)
RAM: Random Access Memory (stack, heap)
I/O address space

## Slide 7: Memory
Example:
  16 KB – flash memory at the top of address space
  4 KB SRAM @ 0x3100
  256 bytes for 8-bit I/O peripherals @ 0x0000
  256 bytes for 16-bit I/O peripherals

## Slide 8: Memory
Flash Memory
--
RAM Memory
16-bit I/Os
8-bit I/Os
--
15 | 14 |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0
0x0000
0x00FE
0x0100
0x01FE
0x0200
0x30FE
0x3100
0x40FE
0xC000
0xFFFE
0x4100
0xBFFE

## Slide 9: MSP430 Stack
LIFO – Last In First Out
SP points to last full location
Grows toward lower addresses

## Slide 10: Data Types
Instructions operating on bytes: suffix .b
Instructions operating on words: suffix .w
Examples

## Slide 11: Instruction Formats
Double-operand
Single-operand
Jumps

## Slide 12: Addressing Modes
Name | Source Operand | Destination Operand
Register |  | 
Indexed |  | 
Symbolic |  | 
Absolute |  | 
Register Indirect |  | 
Autoincrement (Register indirect with autoincrement) |  | 
Immediate |  | 

## Slide 13: Address Specifiers (As, Ad)
As/Ad | Addressing Mode | Syntax | Description
00/0 | Register | Rn | Operand is in register Rn. Instruction specifies register index n.
01/1 | Indexed | X(Rn) | Operand is in memory at the address EA=Rn+X. Instruction specifies register index n and offset X (the next word of instruction)
01/1 | Symbolic | ADDR | Operand is in memory at the address ADDR=EA=PC+X. A special case of indexed mode.
01/1 | Absolute | &ADDR | Operand is in memory at the address X, which is specified in the next instruction word. A special case of indexed mode (Rn=R2, As=01).
10/- | Indirect register | @Rn | Operand is in memory at the address contained in register Rn. The instruction specifies Rn. Applies only to src operand.
11/- | Indirect autoincrement | @Rn+ | Operand is in memory at the address contained in register Rn. After getting the operand, the register is incremented for the size of the operand (1 for byte, 2 for word)
11/- | Immediate | #N | The operand is a constant encoded in the next instruction word. To distinguish from autoincrement, the S-reg is set to PC.

## Slide 14: Register
mov.b r5, r7
mov.w r5, r7
opcode | S-reg | Ad.B/W#.As | D-reg
opcode | S-reg | Ad.B/W#.As | D-reg

## Slide 15: Indexed
mov.w 0x100(r4), 0x200(r5)
opcode | S-reg | Ad.B/W#.As | D-reg

## Slide 16: Symbolic
mov.w A, B
opcode | S-reg | Ad.B/W#.As | D-reg

## Slide 17: Absolute
mov.w &A, &B
opcode | S-reg | Ad.B/W#.As | D-reg

## Slide 18: Register Indirect
mov.w @r5, r7
opcode | S-reg | Ad.B/W#.As | D-reg

## Slide 19: Autoincrement
mov.w @r5+, r7
opcode | S-reg | Ad.B/W#.As | D-reg

## Slide 20: Immediate
mov.w #45, r7
opcode | S-reg | Ad.B/W#.As | D-reg