## Slide 1: CPE 323 Intro to Embedded Computer Systems Assembly Language Programming
Aleksandar Milenkovic
milenka@uah.edu

## Slide 2: Admin

## Slide 3: Assembly Development Flow
ASM file (*.asm)
Assembler
Object File
ASM file (*.asm)
Assembler
Object File
ASM file (*.asm)
Assembler
Object File
Linker
Static Libraries
Executable File
Loader
Machine Code in Memory

## Slide 4: Assembly Language Directives
Assembly language directives tell the assembler to
  Set the data and program at particular addresses in address pace
  Allocate space for constants and variables
  Define synonyms
  Include additional files
  …
Typical directives
  Equate: assign a value to a symbol
  Origin: set the current location pointer
  Define space: allocate space in memory
  Define constant: allocate space for and initialize constants
  Include: loads another source file

## Slide 5: ASM Section Control Directives
Description | ASM430 (CCS) | A430 (IAR)
Reserve size bytes in the uninitialized sect. | .bss | -
Assemble into the initialized data section | .data | RSEG const
Assemble into a named initialized data sect. | .sect | RSEG
Assemble into the executable code | .text | RSEG code
Reserve space in a named (uninitialized) section | .usect | -
Align on byte boundary | .align 1 | -
Align on word boundary | .align 2 | EVEN

## Slide 6: Constant Initialization Directives
.byte
.float
.word
.long
.string

## Slide 7: Directives: Dealing with Constants
b1: .byte 5 ; allocates a byte in memory and initialize it with 5
b2: .byte -122 ; allocates a byte with constant -122
b3: .byte 10110111b ; binary value of a constant
b4: .byte 0xA0 ; hexadecimal value of a constant
b5: .byte 123q ; octal value of a constant
tf: .equ 25

## Slide 8: Directives: Dealing with Constants
...
w1: .word 21 ; allocates a word constant in memory;
w2: .word -21
w3: .word tf
dw1: .long 100000 ; allocates a long word size constant in memory;
; 100000 (0x0001_86A0)
dw2: .long 0xFFFFFFEA

## Slide 9: Directives: Dealing with Constants
s1: .byte 'A', 'B', 'C', 'D‘ ; allocates 4 bytes in memory with string ABCD
s2: .byte "ABCD", ' ' ; allocates 5 bytes in memory with string ABCD + NULL

## Slide 10: Table of Symbols
Symbol | Value [hex]
b1 | 0x3100
b2 | 0x3101
b3 | 0x3102
b4 | 0x3103
b5 | 0x3104
tf | 0x0019
w1 | 0x3106
w2 | 0x3108
w3 | 0x310A
dw1 | 0x310C
dw2 | 0x3110
s1 | 0x3114
s2 | 0x3118

## Slide 11: Directives: Variables in RAM
.bss v1b,1,1 ; allocates a byte in memory, equivalent to DS 1
.bss v2b,1,1 ; allocates a byte in memory
.bss v3w,2,2 ; allocates a word of 2 bytes in memory
.bss v4b,8,2 ; allocates a buffer of 2 long words (8 bytes)
.bss vx,1,1
Label | Address | Memory[15:8] | Memory[7:0]
v1b |  | -- | --
v3w |  | -- | --
v4b |  | -- | --
 |  | -- | --
 |  | -- | --
 |  | -- | --
vx |  |  | 
Symbol | Value [hex]
v1b | 
v2b | 
v3w | 
v4b | 
vx | 

## Slide 12: Decimal/Integer Addition of 32-bit Numbers
Write an assembly program that finds a sum of two 32-bit numbers
  Input numbers are decimal numbers given in BCD (8-digit in length)
  Input numbers are signed integers in two’s complement
E.g.:
lint1: .long 0x45678923
lint2: .long 0x23456789
Label | Address | Memory[15:0]
lsumd | 0x2400 | 0x????
 | 0x2402 | 0x????
lsumi | 0x2404 | 0x????
 | 0x2406 | 0x????
 | . . . | 
 | . . . | 
lint1 | 0x4400 | 0x8923
 | 0x4402 | 0x4567
lint2 | 0x4404 | 0x6789
 | 0x4406 | 0x2345

## Slide 13: Allocate Space & Start Program

## Slide 14: Main Code (Ver. 1)

## Slide 15: Main Code (Ver. 2)

## Slide 16: Count Characters ‘E’ in a String
Write an assembly program that processes an input string to find the number of characters ‘E’ in the string
The number of characters is “displayed” on the port 1 of the MSP430

## Slide 17: Count Characters ‘E’ in a String
;-------------------------------------------------------------------------------
; File : Lab4_D1.asm (CPE 325 Lab4 Demo code)
; Function : Counts the number of characters E in a given string
; Description: Program traverses an input array of characters
; to detect a character 'E'; exits when a NULL is detected
; Input : The input string is specified in myStr
; Output : The port P1OUT displays the number of E's in the string
; Author : A. Milenkovic, milenkovic@computer.org
; Date : August 14, 2008
;-------------------------------------------------------------------------------
.cdecls C,LIST,"msp430.h" ; Include device header file
;-------------------------------------------------------------------------------
.def RESET ; Export program entry-point to
; make it known to linker.
myStr: .string "HELLO WORLD, I AM THE MSP430!", ''
;-------------------------------------------------------------------------------
.text ; Assemble into program memory.
.retain ; Override ELF conditional linking
; and retain current section.
.retainrefs ; And retain any sections that have
; references to current section.
;-------------------------------------------------------------------------------
RESET: mov.w #__STACK_END,SP ; Initialize stack pointer
mov.w #WDTPW|WDTHOLD,&WDTCTL ; Stop watchdog timer

## Slide 18: Count Characters ‘E’ in a String
;-------------------------------------------------------------------------------
; Main loop here
;-------------------------------------------------------------------------------
main:
;-------------------------------------------------------------------------------
; Stack Pointer definition
;-------------------------------------------------------------------------------
.global __STACK_END
.sect .stack
;-------------------------------------------------------------------------------
; Interrupt Vectors
;-------------------------------------------------------------------------------
.sect ".reset" ; MSP430 RESET Vector
.short RESET
.end