## Slide 1: CPE 323 Intro to Embedded Computer Systems Flash Memory
Aleksandar Milenkovic
milenka@uah.edu

## Slide 2: Admin

## Slide 3: MSP430F5529 Block Diagram

## Slide 4: Non-Volatile Memory
Non-volatile memories in MSP430
  Flash
  FeRAM

## Slide 5: Introduction
Default view of Flash memory is Read Only
  Contains code and data constants
In-system programmable (ISP) Flash memory
  Read/write into the Flash memory from the running program
But writing into the Flash requires a special interface
MSP430 flash memory features
  Bit-, byte-, and word-addressable and programmable
  Internal programming voltage generation
  Segment erase and mass erase

## Slide 6: Preliminaries
Floating-gate MOSFET
Two states
  Erase – ‘1’ (no charge)
  Program – ‘0’ (charge on FG)
Read, Write, Erase

## Slide 7: NOR Flash Array

## Slide 8: Flash Memory Properties
Require high voltages for erase and write operations
Write: 1 -> 0 (individual bits), but no 0 -> 1 (erase, entire segment)
Endurance: charges are moved across oxides, wearing them out over time, resulting in a finite number of Program/Erase cycles (PE)
  ~100,000 times in MSP430 flash
Retention: charges can leak out from the FG over time
  ~100 years at room temperature (far less at higher temperatures)

## Slide 9: Flash Memory Physical View
Flash operations
  Read
  Write (Program)
  Erase
Components
  Flash array
  Control, address, and data latch registers
  Flash controller
  Voltage generator (charge pump)
    High voltages are required for program and erase

## Slide 10: Flash Organization
Banks: 64 KB – can be erased
Segments: 512 B – smallest unit that can be erased
  Information Memory segments are 128 B
Long Word/Word/Byte – smallest units that can be read or programmed
  Also writes can be streamed to 128 byte blocks

## Slide 11: Flash Memory Erase/Write Modes
Byte, word, long-word write
Block write (128 B)
Segment erase
Bank erase
Mass erase (all main memory banks)
Read during bank erase (except for the one currently read from)
Can be initiated from within Flash or SRAM

## Slide 12: Erase Cycle
From within flash

## Slide 13: Erase Cycle (cont’d)
Initiated from SRAM

## Slide 14: Byte/Word Write Cycle (cont’d)
Initiated from within flash

## Slide 15: Byte/Word Write Cycle (cont’d)
Initiated from SRAM

## Slide 16: Long Word Write
Initiated from within flash

## Slide 17: Flash Memory Access when BUSY

## Slide 18: Flash Controller Registers: FCTL1

## Slide 19: Flash Controller Registers: FCTL3

## Slide 20: Flash Controller Registers: FCTL4

## Slide 21: Examples
void EraseFlashSegment(uint_16 *pFlashAddress) {
while(FCTL3&BUSY); // Wait while BUSY=1
FCTL3 = FWPW; // Clear LOCK bit
FCTL1 = FWPW + ERASE; // Enable segment erase bit
*pFlashAddress = 0; // Dummy write to erase Flash segment
while(FCTL3&BUSY); // Wait while BUSY=1
FCTL3 = FWPW + LOCK; // Done, set LOCK
}
void ProgramFlashWord(uint_16 *pFlashAddress, uint16 wVal) {
FCTL3 = FWPW; // Clear LOCK bit
FCTL1 = FWPW+WRT; // Enable write
*pFlashAddress = wVal; // Write new value to a flash location
while(FCTL3&BUSY); // Wait while BUSY=1
FCTL1 = FWPW; // Done. Clear WRT bit
FCTL3 = FWPW + LOCK; // Set LOCK
}